## Slide 1: Accumulation of (bio)degradable plastics in soil
CIPA Congress 2018, Arcachon, May 29, 2017

## Slide 2
OWS
Different end-of-life options
Expert statement
TOPICS
(commissioned by European Bioplastics)

## Slide 3
DRANCO technology – UG, 1983 (pilot in 1984)
Founded in 1988
Consolidated sales (2015-2017): 20 million €/yr
Export: 90%
80 employees
Head office: Gent, Belgium
Affiliates: OWS Inc., Dayton, Ohio, USA
DRANCO N.V.
BES GmbH, Germany
Partner: DJK International, Tokyo, Japan
COMPANY PROFILE

## Slide 4
‘One-stop’ laboratory for biodegradability
& compostability testing
Strictly independent
Quality control: ISO 17025
Recognized by all certification
bureaus worldwide
Active in standardization: CEN/ASTM/ISO
Member of several certification committees
& industrial associations (EuBP, BBP,…)
More than 30 years of experience
10,000+ samples tested for 1,250+ clients
CONTRACT RESEARCH LABORATORY

## Slide 5
REFERENCES
Base Polymers | BASF, Bio-Fed, Corbion, Du Pont, FKuR, NatureWorks, Novamont,…
Paper & Board | Ahlstrom, Huhtamaki, Int. Paper, Kuan Chun Paper, Pactiv, UPM,…
Packaging | Alcan Packaging, Amcor, Mondi Packaging, Sealed Air, Tetra Pak,…
Consumer Goods | Henkel, Kimberly-Clark, Lenzing, Nestlé, P&G, Sara Lee, SCA, Unilever,…
Inks & Masterbatches | PolyOne, CIBA, Chimigraf, Flint, Sun Chemical, Wacker,…
Films & Bags | Because We Care, Cortec, Kafrit, Sabic, Sphere, Wuhan Huali,…
Food Service Ware | Medac, Minima, Seda, Smurfit Kappa, Solo Cup,…
Other categories | Smithers-Oasis, EBPA, EuBP,…
Oxo-degradable | CIBA, Goody (ACCC), Wells Plastics, Symphony, EPI, EconVerte,…
Enzyme-mediated | Enzymoplast, ECM, Bio-Tec,…

## Slide 6
OWS
Different end-of-life options
Expert statement
TOPICS

## Slide 7
PRODUCT USE/DISPOSAL
CONTROLLED
UNCONTROLLED
(LITTER or IN SITU)
WASTEWATER
SOLID WASTE
OPEN WATER
SOIL
MARINE
AEROBIC
TREATMENT
COMPOSTING
ANAEROBIC
TREATMENT
BIOGASIFICATION
LANDFILL
USE OF COMPOST IN SOIL
ANAEROBIC
STABILISATION
CENTRAL HOME
ENVIRONMENTAL NICHES
Biodegradable plastics are no solution/excuse for littering!

## Slide 8
60°C
21°C
compost > soil > fresh water > marine water > landfill
anaerobic digestion
AGGRESSIVENESS OF ENVIRONMENT

## Slide 9
compost > soil > fresh water > marine water > landfill
anaerobic digestion
Fungi + Bacteria + Actinomycetes
Bacteria only
(Fungi inactive)
Multiple Bacteria
AGGRESSIVENESS OF ENVIRONMENT

## Slide 10
BIODEGRADATION vs. ENVIRONMENTAL NICHE
High T
(50-60°C)
AEROBIC (WATER) + ANAEROBIC
BACTERIA, NO FUNGI
AEROBIC (COMPOST & SOIL)
BACTERIA & FUNGI
Chemical pulp
Starch
PLA
Starch/PCL
PHA
Chemical pulp
Starch
Starch/PCL
PHA
Chemical pulp
Mechanical pulp
Starch
PLA
Starch/PCL
PHA
PBAT
PBAT
PHA
Starch/PCL
Starch
Chemical pulp
Mechanical pulp
Low T
(≤ 35 °C)
THERMOPHILIC
DIGESTION
INDUSTRIAL
COMPOSTING
MESOPHILIC
DIGESTION
WATER
HOME
COMPOSTING
SOIL

## Slide 11
Revision of the EU Fertilisers Regulation
Mulching films
Controlled release fertiliser coatings
Growth media
(Body bags)
European standard EN17033
Heavy metals & Fluorine content
Biodegradation
Plant toxicity
Earthworm toxicity
Toxicity towards micro-organisms
No disintegration!
RELEVANT LEGISLATION & STANDARDS
Environmental safety!

## Slide 12
OWS
Different end-of-life options
Expert statement
  What is “complete” biodegradation?
  Accumulation of plastics in soil
TOPICS

## Slide 13
Only scientific correct parameter is conversion to CO2
General opinion: “complete” = 100%
Biochemical pathway of biodegradation:
Cpolymer + O2  CO2 + H2O
“COMPLETE“ BIODEGRADATION
Biomass growth
Intermediate degradation products
+ Cresidual + Cbiomass
Not all Cpolymer is converted to CO2!

## Slide 14
Biochemical pathway of biodegradation:
Cpolymer + O2  CO2 + H2O + Cresidual + Cbiomass
EN 17033 (2018) standard on soil biodegradation :
complete biodegradation = 90% (absolute or relative)
“COMPLETE“ BIODEGRADATION
Cannot be quantified
Can be quantified

## Slide 15
“COMPLETE“ BIODEGRADATION – Cbiomass
± 10%
10-15%
± 25%
Straw: 25-30%
Wood fibers, birch leaves, pine needles: up to 40%
Cbiomass typically varies between 10% and 40%

## Slide 16
(LD)PE mulching film (15-50 µm)
Removal is costly and labor intensive
Contamination hinders recycling
Accumulation increases with decreasing thickness1:
  25µm PE film: 10% remains in/on soil
  20µm PE film: 25% remains in/on soil
  10µm PE film: 68% remains in/on soil
Soil biodegradable mulching film (15 µm)
No need for removal
Complete biodegradation within maximum 2 years under laboratory conditions
1: APE Europe (Agriculture Plastic Environment), industry association for the non-packaging agri-plastics presentation by Bernard Le Moine at Agricultural Film 2014
ACCUMULATION IN SOIL

## Slide 17
ACCUMULATION IN SOIL
20 µm LDPE film – 1 cultivation period/year
463 kg/hectare after 10 years
4.6 tonnes/hectare after 100 years
(accumulation continues over time)
15 µm soil biodegradable film – 1 cultivation period/year
188 kg/hectare after the first year
281 kg/hectare after the second year
(= maximum accumulation level!)

## Slide 18
ACCUMULATION IN SOIL
4.6 tonnes

## Slide 19
ACCUMULATION IN SOIL
What if cultivation is ceased every two years?

## Slide 20
Complete biodegradation does not mean “100% conversion to CO2”.
Conventional (LD)PE mulching films accumulate at a rate of 463 kg per hectare per decade1.
Soil biodegradable mulching films have a maximum accumulation level of 281 kg per hectare1, returning to no accumulation if cultivation is ceased for two years.
(LD)PE mulching films cannot be downgauged as this increases the relative level of contamination and decreases the recovery rate.
1: Assuming one cultivation period per year and a thickness of 20 µm for LDPE and 15 µm for soil biodegradable mulching films
CONCLUSIONS

## Slide 21: THANK YOU FOR YOUR ATTENTION
OWS nv, Dok-Noord 5, B-9000 Gent, Belgium
Email: sam.deconinck@ows.be
Website: www.ows.be